OpenBMC
An open framework of embedded Linux in server management
Chester Lin
SUSE Labs

---
What’s BMC?
- Baseboard Management Controller
- A monitoring and control unit inside the sever board.
  - Sensor monitoring and thermal control.
    - Temperature, Voltage/Current, Fan, Power Consumption / Status, .. etc.
  - Power Management:
    - Power control based on ACPI power states.
    - Power Capping / CPU throttling (Need to corporate with CPU or Power Management IC or SoC such as Intel ME)
  - Remote Management
    - IKVM (USB-HID + Graphics), Virtual Storage (USB-Mass-Storage)
    - Management Interfaces: IPMI, Redfish, Web, SNMP, CLI, SSH, etc.
    - Serial Over LAN.
  - Hardware / Firmware Inventory
    - Part number, version, manufacturer, SMBIOS, hardware locations, etc.,
[Speaker Notes: BMC has been developed since 90’s, which is used for computer system management, especially servers.]

---
What’s BMC?
- A monitoring and control unit inside the sever board
  - Critical event alerts, logging & fail-overs
    - Fan fail, PSU fail, system overheat, … etc.
    - System-wide watchdog, CPU crash dump logging, OS-level events.
  - Storage management.
    - Disk Status, Disk hot-plug, RAID configuration, .. etc.
  - Device hot-plug
    - Compute Node / CPU / Memory / PCI-E devices, .. etc.
  - Firmware Management
    - Firmware Update: UEFI/ME/LAN/FPGA, .. etc.
    - UEFI configurations such as BootOrder.

---
Hardware connections of BMC
Other Connections:
USB, PCH, ADC, PECI, ..
*source: IPMI 2.0 spec
[Speaker Notes: A BMC can connect with many interfaces: NIC, UART, I2C Most of BMC chips include VGA core. (Host screen and IKVM)]

---
Software stack of BMC
- A Linux-based embedded system. (RTOS in the past)
- Integrates lots of open source packages.
  - Linux Kernel, U-Boot, GCC tool-chain, GLIBC, busybox, Third-Party Authentication, crypto and security-related applications [e.g, TLS, PKI, Firewalls], Dynamic DNS, NTP, .. etc.
- Multiple management interfaces are provided.
  - IPMI
    - Supported by server industries.
    - Multiple channels: LAN, KCS/BT, UART, I2C, etc.
  - CLI / SNMP / SSH
  - Redfish (Managed by DMTF)
    - The successor of IPMI
    - Higher security implementations.
    - RESTful Framework
    - Scalable API design.

---
Software stack of BMC
WEB-UI

---
Why OpenBMC?
- Eliminates the difficulties of maintaining proprietary BSPs. [Close → Open]
- Source codes can be mainly managed by upstream.
- Managed by Linux Foundation.
OpenBMC
Traditional
Linux
kernel
Boot
Loader
SoC
Codes
Boot
Loader
Linux
kernel
SoC
Codes
OSS
Package
Server’s
device-tree/
drivers
Chip
Vendor
BSP
OSS
Package
FW
Vendor
BSP
OpenBMC
OSS
Package
FW
Vendor
BSP
OSS
Package
Server
Vendor
BSP
OSS
Package
OSS
Package
Server
Vendor
BSP

---
Why OpenBMC?
- Provides a reference framework based on Yocto.
  - Unifies interfaces so that the management software can work across different vendors’ BMC firmware instances.
Brand-A
Whitebox
Brand-B
*Icon source: https://freeicons.io

---
Software Framework
- OpenEmbedded Core
- Yocko-Poky
  - BitBake
- Meta layers

---
Build System
BitBake: An automation build tool based on Python3.
Fetch
Pkg1-code
from SCM
meta-A
Bit
Bake
recipe-pkg1
recipe-pkg2
Pkg2-code
from local
configs,
Scripts,
Patches
Pkg1
Build
Pkg1
Install
Target
Image

---
Package repo
- GitHub: https://github.com/openbmc
  - Most of public repositories are under this project.
    - https://github.com/openbmc/openbmc
    - https://github.com/openbmc/bmcweb
    - https://github.com/openbmc/linux
    - https://github.com/openbmc/phosphor-dbus-interfaces
    - …..
  - Major languages: C++14, C, BitBake, Shell and Python
  - Other branches:
    - Facebook: https://github.com/facebook/openbmc
    - AMI: https://github.com/ami-megarac/MORF-OpenBMC
    - OpenBMC CI: https://openpower.xyz/

---
File Tree Examples
LCONF_VERSION = "8"
BBPATH = "${TOPDIR}"
BBFILES ?= ""
BBLAYERS ?= " \
  ##OEROOT##/meta \
  ##OEROOT##/meta-openembedded/meta-oe \
  ##OEROOT##/meta-openembedded/meta-networking \
  ##OEROOT##/meta-openembedded/meta-perl \
  ##OEROOT##/meta-openembedded/meta-python \
  ##OEROOT##/meta-phosphor \
  ##OEROOT##/meta-aspeed \
  ##OEROOT##/meta-openpower \
  ##OEROOT##/meta-ibm \
  ##OEROOT##/meta-ibm/meta-romulus \
  "
- IBM/Romulus
meta-ibm/meta-romulus/
├── conf
│   ├── bblayers.conf.sample
│   ├── conf-notes.txt
│   ├── distro
│   │   └── openbmc-romulus.conf
│   ├── layer.conf
│   ├── local.conf.sample
│   └── machine
│   └── romulus.conf
KMACHINE = "aspeed"
KERNEL_DEVICETREE = "${KMACHINE}-bmc-opp-${MACHINE}.dtb"
UBOOT_MACHINE = "ast_g5_ncsi_config"
PREFERRED_PROVIDER_virtual/p9-vcs-workaround = ''
require conf/machine/include/ast2500.inc
require conf/machine/include/obmc-bsp-common.inc
require conf/machine/include/openpower.inc
require conf/machine/include/p9.inc

---
File Tree Examples
meta-ibm/meta-romulus/
……………….
├── recipes-kernel
│   └── linux
│   ├── linux-aspeed
│   │   └── romulus.cfg
│   └── linux-aspeed_%.bbappend
├── recipes-phosphor
│   ├── chassis
……………….
│   │   ├── vrm-control
│   │   │   ├── vrm-control@.service
│   │   │   ├── vrm-control.sh
│   │   │   └── vrm.sh
│   │   └── vrm-control.bb
……………….
│   ├── sensors
│   │   ├── phosphor-hwmon
│   │   │   └── obmc
│   │   │   └── hwmon
│   │   │   ├── ahb
│   │   │   │   └── apb
│   │   │   │   ├── bus@1e78a000
│   │   │   │   │   └── i2c-bus@440
│   │   │   │   │   └── w83773g@4c.conf
│   │   │   │   └── pwm-tacho-controller@1e786000.conf
- IBM / Romulus
  - recipes
  - .bb
  - .bbappend

---
Build Examples
- Set TEMPLATECONF
  - export TEMPLATECONF=meta-ibm/meta-romulus/conf
  - Workdir: openbmc/build/
- Run BitBake
  - bitbake obmc-phosphor-image
- Output files and binaries
  - build/tmp/deploy/images/romulus

---
Running services in OpenBMC

---
Softwre Stack - IPMI daemon
Source:
openBMC docs

---
Softwre Stack - HTTPS applications
config
D
B
U
S
Angular.js
Event
monitor
crow
phorsphor-webui
Web UI
IKVM
sensor
VirtualMedia
ikvm
bmcweb
User
mgmt
….
Web
Openbmc REST
Redfish
IKVM
[Speaker Notes: bmcweb is a http server which is originally developed and used in OpenPower platforms.]

---
Softwre Stack - OpenBMC REST
curl -k -X GET https://root:0penBmc@${bmc}:${bmcport}/xyz/openbmc_project/network/eth0/enumerate
      "data": {
        "/xyz/openbmc_project/network/eth0": {
        "AutoNeg": false,
        "DHCPEnabled": true,
        "DomainName": [],
        "IPv6AcceptRA": false,
        "InterfaceName": "eth0",
        "LinkLocalAutoConf": "xyz.openbmc_project.Network.EthernetInterface.LinkLocalConf.both",
        "MACAddress": "52:54:0:12:34:56",
        "NTPServers": [],
        "Nameservers": [],
        "Speed": 0
        },
        "/xyz/openbmc_project/network/eth0/ipv4/49e97e86": {
        "Address": "10.0.2.15",
        "Gateway": "",
        "Origin": "xyz.openbmc_project.Network.IP.AddressOrigin.DHCP",
        "PrefixLength": 24,
        "Type": "xyz.openbmc_project.Network.IP.Protocol.IPv4"
        },
        "/xyz/openbmc_project/network/eth0/ipv6/ff024971": {
        "Address": "fe80::5054:ff:fe12:3456",
        "Gateway": "",
        "Origin":
        "xyz.openbmc_project.Network.IP.AddressOrigin.LinkLocal",
        "PrefixLength": 64,
        "Type": "xyz.openbmc_project.Network.IP.Protocol.IPv6"
        }
      },
      "message": "200 OK",
      "status": "ok"

---
YAML
- Two major types of yaml files in OpenBMC
  - Defines schematics of services
    - Properties, methods and parameters, enumerations, errors, .. etc.
  - Interface descriptors
    - *.interface.yaml
  - Error descriptors
    - *.errors.yaml, *.metadata.yaml

---
YAML Example – Watchdog Interface
description: >
    Implement the watchdog function.
methods:
    - name: ResetTimeRemaining
      description: >
        Resets the time remaining to the configured interval. ....
      parameters:
        - name: EnableWatchdog
        type: boolean
        description: >
        If true the watchdog will be enabled when the reset is performed.
      errors:
        - xyz.openbmc_project.Common.Error.InternalFailure
properties:
……….
    - name: Enabled
      type: boolean
      description: >
        The watchdog is enabled or not.
      default: false
    - name: ExpireAction
      type: enum[self.Action]
      description: >
        The action the watchdog should perform when it expires.
      default: 'HardReset'
    - name: Interval
      type: uint64
      description: >
        Time interval to arm the watchdog,
        in milli-second.
      default: 30000
    - name: TimeRemaining
      type: uint64
      description: >
        Time remaining before timeout, ……
……….
enumerations:
   - name: Action
     description: >
       The type of action to perform.
     values:
       - name: 'None'
        description: >
        Do nothing.
       - name: 'HardReset'
        description: >
        Perform a reset of the system.
       - name: 'PowerOff'
        description: >
        Perform a power off of the system.
       - name: 'PowerCycle'
        description: >
        Perform a power cycle of the system.

---
YAML – Common Errors
- name: Timeout
  description: Operation timed out.
- name: InternalFailure
  description: The operation failed internally.
- name: InvalidArgument
  description: Invalid argument was given.
- name: InsufficientPermission
  description: Insufficient permission to perform operation
- name: NotAllowed
  description: The operation is not allowed
- name: NoCACertificate
  description: Server's CA certificate has not been provided.
- name: Timeout
  meta:
    - str: "TIMEOUT_IN_MSEC=%llu"
      type: uint64
- name: InvalidArgument
  meta:
    - str: "ARGUMENT_NAME=%s"
      type: string
    - str: "ARGUMENT_VALUE=%s"
      type: string
- name: InternalFailure
  level: ERR
- name: InsufficientPermission
  level: INFO
- name: NotAllowed
  level: INFO
  meta:
    - str: "REASON=%s"
      type: string
- name: NoCACertificate
  level: ERR

---
YAML
.yaml
FuncA/
Server.cpp
& hpp
Method
Properties
Properties
Service1
Properties
Method
Parameters
Method
FuncB/
Server.cpp
& hpp
Parameters
Parameters
Enumeration
Parameters
Enumeration
Parameters
Service2
Parameters
Parameters
libphosphor_
dbus.so.0
Parameters
signals
signals
Parameters
Parameters
Parameters
FuncC/
Server.cpp
& hpp
Service
3
Parameters
….
…..
Types of properties / parameters:
int16/32
array []
byte
boolean
dict [,]
string
…..
path
uint16/32

---
Service Construction
phosphor-dbus-interfaces/../User/Manager.interface.yaml
- name: CreateUser
      description: >
        …………..
      parameters:
        - name: CreateUser
        type: string
        - name: GroupNames
        type: GroupNames
        - name: Privilege
        type: string
        - name: Enabled
        type: boolean
        ……………………...
build/../User/Manager/server.cpp
sdbus++
phosphor-user-manager/user_mgr.hpp

---
The calls from clients
phosphor-host-ipmid/user_channel/user_mgmt.cpp
createUserMethod =
"CreateUser"
# busctl introspect xyz.openbmc_project.User.Manager /xyz/openbmc_project/user xyz.openbmc_project.User.Manager

---
Sensor
- Based on Linux hwmon
D
B
U
S
Server.cpp
WEB
.config files under
/etc/default/obmc/hwmon
Interface
[Value]
REST
Load parameters, such as
sysfs-path, hwmon-names,
indexes, intervals, thresholds,
gpio settings… etc.
Update
Sensor
Interfaces(..);
Phosphor-
hwmon-readd
Server.cpp
IPMI
Interface
[Warning]
……….
Console
Server.cpp
Hwmons
(temp, fan, in,
curr, power)
Interface
[Value]
……….

---
Sensor Example
Fan RPM Reading in IBM Romulus (OpenPower)
recipes-phosphor/sensors/
phosphor-hwmon_%.bbappend
openbmc/meta-ibm/meta-romulus/
recipes-phosphor/sensors/phosphor-hwmon/obmc/ahb/apb/pwm-tacho-controller@1e786000.conf
etc/default/obmc/hwmon/ahb/apb/pwm-tacho-controller@1e786000.conf
BitBake
LABEL_fan9 = "fan0"
LABEL_fan11 = "fan1"
LABEL_fan13 = "fan2"
PWM_TARGET_fan9 = "1"
PWM_TARGET_fan11 = "2"
PWM_TARGET_fan13 = "1"
LABEL_fan9 = "fan0"
LABEL_fan11 = "fan1"
LABEL_fan13 = "fan2"
PWM_TARGET_fan9 = "1"
PWM_TARGET_fan11 = "2"
PWM_TARGET_fan13 = "1"
Install
read config
/sys/devices/platform/ahb/ahb:apb/
1e786000.pwm-tacho-controller/
hwmon/hwmon0:
fan9_input
fan11_input
fan13_input
Phosphor-
hwmon-readd
find
Read
Kernel-src:
drivers/hwmon/aspeed-pwm-tacho.c

---
Kernek Device Tree
LABEL_fan9 = "fan0"
LABEL_fan11 = "fan1"
LABEL_fan13 = "fan2"
PWM_TARGET_fan9 = "1"
PWM_TARGET_fan11 = "2"
PWM_TARGET_fan13 = "1"
fan[1-*]_input	Fan input value.
        Unit: revolution/min (RPM)
        RO

---
SW/FW Information & Update
- REST Interface
  - /xyz/openbmc_project/software/<id>
  - Multiple software instances.
- Update channels
  - Network
    - Scp the image to tmp/images/
    - OpenBMC REST APIs
      - File Upload
      - TFTP Download
  - InBand
    - LPC (Low Pin Count)
    - I2C
    - P2A (PCI-TO-AHB MMIO)
  - Redfish

---
Firmware Update Flow
openbmc/phosphor-bmc-code-mgmt
RSA+SHA256
*Source:
openbmc docs

---
Linux Kernel & U-Boot
- ASPEED is currently the most popular BMC CPU vendor adopted by OpenBMC.
- Most ASPEED drivers are merged into upstream in recent years. [keyword: aspeed ]
  - Kernel:
    - clk, edac, gpio, drm, hwmon, i2c, iio, mtd, media, pinctrl, rtc, tty, usb_gadget, kcs for ipmi.. etc.
  - U-Boot
    - /arch/arm/mach-aspeed, board/aspeed, drivers/clk/aspeed, drivers/pinctrl/aspeed,
- Different platforms needs different device-trees.
  - /arch/arm/boot/dts/openbmc-flash-layout.dtsi
  - /arch/arm/boot/dts/aspeed-bmc-*.dts
    - e.g, opp (OpenPower), arm, facebook-specific, … etc.

---
Devicetree

---
Devicetree

---
Firmware Security
- Signed firmware validation while updating.
  - Implements sign (RSA+SHA256) and verify based on OpenSSL
  - Firmware Update Validation
- User Management
  - Linux PAM
  - LDAP (Kerberos?)
  - Distinguished roles and privileges
    - Group roles: ssh, ipmi, redfish web
    - Privileges: admin, operator, user, callback

---
Firmware Security
- Certificate Manager
  - Phosphor-certificate-manager
    - manages all certificates that openBMC might needs, such as https, LDAP.
- Network sessions.
  - HTTPS(WEB), RESTful (OpenBMC REST/Redfish)
  - IKVM / Virtual Media
  - IPMI-RAKP, IPMI Serial-Over-LAN
- Security Response Team
  - https://github.com/openbmc/docs/blob/master/security/obmc-security-response-team.md

---
Market Opportunities of SUSE
- Unify firmware update framework based on OpenBMC APIs or Redfish APIs through In-Band and Out-Band channels.
  - UEFI, Intel Node Manager, SAS controller FW, NIC controller FW, FPGA flash, etc.
- Integrates OpenBMC interfaces with SUSE manager to have more detailed management on hardware and firmware resources.
  - Hardware / Firmware status monitoring and Inventory management during system offline.
  - Scalability of firmware deployment.
  - Device management [e.g, Hotplug]

---
u-bmc
- Another BMC FW infrastructure based on u-root
  - Use gRPC instead of IPMI
    - Protobuf: https://developers.google.com/protocol-buffers/
  - U-root implements Linux userspace bsed on Golang.
  - Support QEMU simulation.
  - https://github.com/u-root/u-bmc

---
Q&A

---
Title of Logo Slide Here (32pt)
Subtitle Here (20pt)
- First-level bullet (24pt)
  - Second-level bullet (20 pt)
    - Third-level bullet (16pt)
      - Fourth-level bullet (14pt)

---
Backup

---
Template Instructions
This slide outlines the basic guidelines and instructions to help you use the SUSE® presentation template.
- Delete this slide and all guideline slides (1–7) before projecting, presenting or sending to a client.
- When inserting slides into this template from other presentations, you will need to go to the template's master page and update each inserted slide so it reflects the SUSE style.
- If you are converting charts and diagrams from Microsoft PowerPoint to OpenOffice.org Impress, you may not be able to edit them once they are in the .ODP format. If this is the case, the graphic must be recreated.
- The goal of this template is to maintain a clear, professional and consistent tone and appearance among all SUSE presentations. The default text boxes in the presentation represent the margins or “working area” to which all text, graphics and diagrams should conform. These margins are not arbitrary, and they are not meant to constrict creativity; when used correctly, they keep the slides focused and leave enough white space so audiences can easily digest the presented material. If you need more room than the margins allow, we suggest moving content to another slide.

---
Color Palette
Colors: Approved RGB colors for SUSE® presentations have been outlined to ensure
color accuracy.
Margins: The gray dotted-line box represents the margins or “working area” to which all text, graphics and diagrams should conform.
How to Add SUSE Colors to Your
LibreOffice Color Palette:
1. Go to the “Tools” menu
2. Select “Options”
3. Expand “LibreOffice”
4. Select “Colors”
5. Delete existing colors (one by one)
6. Add SUSE Colors by giving them a name
and entering RGB values
7. Click “OK”
For more information on SUSE color palette guidelines, visit
https://innerweb.novell.com/brandguide/color
RGB
122, 193, 66
Medium
Green
RGB
69, 76, 81
Dark
Neutral
RGB
106, 115, 123
MD/Dark
Neutral
RGB
148, 160, 169
Medium
Neutral
RGB
228, 229, 230
Light
Neutral
RGB
239, 240, 240
Tint
Neutral
RGB
0, 174, 239
Bright
Blue
RGB
0, 127, 178
Dark
Blue
RGB
99, 202, 225
Medium
Blue
RGB
173, 224, 238
Light
Blue
RGB
221, 241, 247
Tint
Blue
RGB
193, 216, 47
Bright
Green
RGB
67, 149, 57
Dark
Green
RGB
122, 193, 66
Medium
Green
RGB
208, 228, 166
Light
Green
RGB
235, 246, 220
Tint
Green
RGB
248, 152, 29
Bright
Orange
RGB
227, 127, 28
Dark
Yellow
RGB
247, 172, 7
Medium
Yellow
RGB
255, 212, 87
Light
Yellow
RGB
255, 246, 212
Tint
Yellow
RGB
255, 221, 0
Bright
Yellow
RGB
90, 154, 152
Dark
Teal
RGB
114, 174, 182
Medium
Teal
RGB
195, 223, 224
Light
Teal
RGB
216, 233, 232
Tint
Teal
RGB
236, 0, 140
Bright
Magenta
RGB
54, 60, 116
Dark
Purple
RGB
84, 98, 145
Medium
Purple
RGB
181, 187, 212
Light
Purple
RGB
222, 230, 243
Tint
Purple
RGB
237, 28, 36
Bright
Red
RGB
0, 111, 102
Blue-
Green

---
Graphics and Typeface
Primary Icon Color
Icons: Icon libraries are available for download in bubble and 3-D designs. The primary color for SUSE is green.
Typeface: Arial is the typeface for all SUSE presentations.
Bubble
3-D
How to Add SUSE Icons to LibreOffice Gallery:
1. Go to the “Tools” menu
2. Select “Gallery”
3. In the Gallery window select “New Theme ...”
4. With the “General” tab active, name
your new theme (e.g., Red flat)
5. Select the “Files” tab
6. Select “Find Files ...”
7. Find the downloaded folder containing
the named icons and click “Select”
8. Select “Add All” and then “OK”
9. Repeat for all icon groups
To download icons, visit:
http://innerweb.novell.com/brandguide/icon.html

---
Editorial Guidelines
To help you achieve a consistent, professional message, general guidelines about SUSE style and grammar usage are outlined below.
Acronyms: Acronyms may be used for industry terms provided you spell out the terms at first reference in body copy:
  1. Example: The Independent Software Vendor (ISV) solution …
  2. Do NOT abbreviate product names in external presentations
- Capitalization: The title of the presentation and the title and subtitle of each slide are the only elements that should be capitalized in title case. All other elements should be capitalized in sentence case (only the first word of each sentence capitalized). This includes bullet points, call outs, emphasized words, table headings and captions.
- Hyphenated compounds within titles: If a hyphenated compound appears in a title, capitalize the word following the hyphen; for example, “Low-Cost Alternatives” would be capitalized as shown.
- Bulleted lists: To set off the lead text in bulleted lists (the words “Bulleted lists” in this case), use colons. Try to keep information presented in bulleted lists short, so it is easy for audiences to consume.
- Punctuation within bulleted lists: Be consistent when punctuating bulleted lists. For example, if you choose to use a complete sentence in the first bullet, use complete sentences, and punctuate accordingly for all bullets on that slide.
- General punctuation: Use “and” instead of “&” except in proper names (e.g., AT&T). Write out
  percent signs.

---
Slide Trademarking Guidelines
The following guidelines are basic rules for product naming and trademarking:
–	Product naming: Use the full legal product name at all references within the presentation; no product acronyms or abbreviations are allowed.
–	Product trademarking: SUSE® products and selected technologies should be trademarked at first reference on each slide. This will help us legally protect these marks.
–	General trademarking: Each slide should be trademarked separately in case the slide is used in multiple decks or pulled from one slide deck to another. (This differs from the usual guideline of trademarking the first reference of a product or technology in a document.)‏
–	Third-party trademarking: Except for Attachmate®, NetIQ® and Novell®, SUSE does not reference
third-party trademarks.
–	Trademark design: Trademarks should be large enough to be recognized, but small enough so they do not distract from the content.
–	Trademark placement: The registered trademark symbol (®) should go on the baseline of the text. The trademark and service mark symbols (™, SM) should be arranged so that the top of the symbol is level with the top of the last letter of the word being marked.