An introduction to SCMI
SUSE Labs - Hardware Enablement - Taipei Team
Presented-by: Chester Lin <clin@suse.com>

---
System Control and Management Interface
What is SCMI?
Standard SW interfaces
Common protocols/APIs that SCMI clients can follow.
Resource Mgmt
HW Abstraction
It has certain rules to control and manage platform/hardware resources.
SCMI clients don’t need to know sophisticated hardware knowledge.
ARM SCMI
Platform Security
Driver instances can be protected in the SCMI server of the secure world.

---
System Control and Management Interface
Overview
* Image source:
Arm SCMI Platform Design Document Ver 3.1
(Doc# DEN0056D)
(Non-Confidential)

---
SCMI Protocols
Base
 Discovers platform information. Such as protocol version, vendor name, supported protocols, set device/protocol permissions and agent configuration reset.
Power Domain Management
Put device/domain to different power saving sates.
Clock Management
Get/Set clocks, clock rate change notification.
Sensor Management
Sensor readings, events and settings.
Reset Domain Management
Device/Domain reset handling and notifications.
Voltage Domain Management
Mode[ON/OFF] config, voltage level config.
Power Capping and Monitoring
Set power caps and monitor power consumptions.
Pin Control
Pin config set/get, pin function select.
NEW in SCMI v3.1
NEW in SCMI v3.2
NEW in SCMI v3.0

---
SCMI Transports (1/2)
- Shared Memory based Transport
  - Poll-based vs Interrupt-Based
Client
Server
Client
Server
Wait for channel free
prepare tx req
prepare tx req
ring doorbell
(e.g. SMC or mailbox)
ring doorbell
(e.g. SMC or mailbox)
process tx req
process tx req
shm
shm
prepare rx resp
prepare rx resp
Wait in poll mode
Completion INT
ISR:
process rx resp
channel free
channel free
process rx resp

---
SCMI Transports (2/2)
- ACPI-baed Transport
  - Transmit SCMI data via ACPI PCCT [Platform Communications Channel Table] type 03.
  - E.g. ACPI methods can store SCMI requests based on the shmem message format via the PCC table type 3.
- Shared Memory or MMIO based Transport for FastChannels
- Virtio-SCMI
  - “Add SCMI server support in guest VM” https://linaro.atlassian.net/browse/SCMI-21
    - e.g. Running SCP FW on vhost-user as SCMI server/backend (QEMU)
    - https://github.com/vingu-linaro/SCP-firmware
  - Defined in OASIS Virtio Spec
    - https://github.com/oasis-tcs/virtio-spec/tree/master/device-types/scmi

---
SCMI Communication
Examples of how SCMI agents can communicate with the SCMI server

---
* Image source:
Arm SCMI Platform Design Document Ver 3.2
(Doc# DEN0056D)
(Non-Confidential)
Channels
- Agent to Platform (A2P)
  - Synchronous & Asynchronous
- Platform to Agent (P2A)
  - Delayed response
    - e.g. clock-rate set complete, reset complete ...
  - Notifications
    - System power events [shutdown, power-up, suspend, cold/warn reset.. etc]
- FastChannel
  - Unidirectional for reducing command latency. (Async and NO return)
  - No message header required but it’s only available for specific cmds in Perf and PowerCap protocols

---
SCMI client-server connections
Client to server that handled by Trusted OS
Normal World
Secure World
EL0
Operating System
Trusted OS [e.g. OPTEE]
SCP Firmware (@BL2)
EL1
Pseudo Trusted App for SCMI
SCMI drivers
(power, clk, reset, .. )
SCMI Server
SCMI protocols
EL2
SCMI Transports
shmem
EL3
EL3 Firmware (e.g. TF-A)
SMC
Handler
SMC Call as Doorbell

---
SMC / HVC calls
* Doc: ARM DEN 0028E - SMC Calling Convention v1.4
SMC Calling Convention (SMCCC)
Bits	Description
31	1’b = Fast Calls (atomic) 0’b = Yield Calls (non-blocking)
30	0’b = SMC32/HVC32, 1’b = SMC64/HVC64
29:24	Service call ranges. / 0: Arm arch, 1: CPU 2: SiP 3: OEM 4: Standard / 5: Stand hypervisor 6: Vendor-specific Hypervisor 7-47: Reserved 48-49: Trusted App 50-63: Trusted OS
23:17	0 for fast calls.
16	A hint bit to denote SVE live state (since SMCCC v.3)
15:0	Function Identifiers

---
SCMI client-server connections
Client to server handled by EL3 firmware
Normal World
Secure World
EL0
Operating System
EL1
SCP Firmware
(@BL2)
SCMI drivers
(power, clk, reset, .. )
SCMI protocols
EL2
SCMI Transports
shmem
EL3 Firmware (e.g. TF-A)
EL3
SMC
Handler
Runtime services for SCMI server
SMC Call as Doorbell

---
SCMI client-server connections
SCMI sessions go through hypervisor
Normal World
Secure World
EL0
Operating System
EL1
SCMI Stack
HVC Call
Hypervisor
EL2
EL3 Firmware (e.g. TF-A)
EL3
SCP Firmware
SMC
Handler
SMC Call
Dedicated
Channel

---
SCMI client-server connections
SCMI sessions via virtio
Normal World
Secure World
EL0
vhost-user back-end
vhost-user front-end (OS)
SCMI Server
e.g. scp-fw VM
SCMI Protocols
EL1
Virtio Trans.
SCMI Virtio Transport
channel
Hypervisor
EL2
EL3
Dedicated Channel
SCP

---
SCMI Stack in Linux kernel

---
SCMI stack in Linux kernel
Core
Subsystems
SysPower
(scmi_power_controll.c)
Clock
(clk-scmi.c)
Sensor
(scmi-hwmon.c)
PowerCap
(scmi-powercap.c)
Reset
(reset-scmi.c)
Common drivers
PwrDomain
(scmi_pm_domain.c)
Performance
(scmi-cpufreq.c)
Sensor
(scmi_iio.c)
Voltage (scmi-regulator.c)
In subsys
folders
bus.c
driver.c
power.c
clock.c
sensors.c
powercap.c
reset.c
Protocols
notify.c
msg.c
scmi_pm_domain.c
perf.c
base.c
voltage.c
(/drivers/firmware/arm_scmi/)
shmem.c
mailbox.c
virtio.c
virtio.c
Transports
optee.c
(/drivers/firmware/arm_scmi/)

---
1
ARM Juno
Devicetree examples
From upstream kernel
&mailbox {
       compatible = "arm,mhu-doorbell", "arm,primecell";
       #mbox-cells = <2>;
};
2
I.MX8ULP
0xC2000000-0xC200FFFF:
SMC64
SiP Service Calls
dt-binding schema:
devicetree/bindings/firmware/arm,scmi.yaml

---
SCMI bus/core init in Linux kernel
3
Core
Protocol driver init
1
IDR:scmi_protocols
firmware {
    scmi {
        compatible = "arm,scmi-smc";
        arm,smc-id = <0xc20000fe>;
        ….
    }
}
scmi_bus_init()
scmi_driver_init()
….
….
….
….
platform_driver_register(
&scmi_driver)
scmi_probe()
2
(*ID array of struct scmi_protocol)
0x10: scmi_base
0x11: scmi_power
….
0x14: scmi_clock
….
0x15 scmi_powercap
scmi_base_register()
scmi_clock_register()
scmi_power_register()
….
….
scmi_powecap_register()
4
5
DT

---
SCMI-based driver register/probe in Linux kernel
Scmi
Protocl
bus
SCMI-based subsys driver
(clk, reset, pd, perf .. etc)
SCMI bus driver
SCMI core: scmi_probe()
notifiers register
scmi_handle/channel/transport setup
scmi_driver_register()
scmi_device_request_notifier()
F
If the prot_id is not in IDR active_protocols yet.
T
If the prot_id is in IDR active_protocols.
Parsing
DT
Save prot_ids in IDR active_protocols
scmi_create_protocol_devices()
F
If the device is registered.
If the device is not yet
registered.
T
__scmi_device_create()
IDR:scmi_protocols
driver_register()
(*ID array of struct scmi_protocol)
0x10: scmi_base
0x11: scmi_power
….
0x14: scmi_clock
….
0x15 scmi_powercap
struct scmi_device initialize
BUS_NOTIFY_
BIND_DRIVER
device_register()
Call registered driver probe()
scmi_bus_notifier()
call_driver_probe()
handle_devm_protocol_get()→
…. →
pi->proto->instance_init()
scmi_set_handle()→
scmi_device_link_add()

---
common
sync
SCMI message handling in Linux kernel
async
ops
 flag
SCMI subsys driver
SCMI protocol driver
SCMI Core
SCMI Transport
do_xfer() [*sync/poll]
scmi_xxx_proto_ops
e.g. clk_ops->rate_get()
registered proto ops
e.g. scmi_clock_rate_get()
send_message() op
e.g. smc_send_message()
info→desc→ops→send_message()
poll_done() op
e.g. mailbox_poll_done()
scmi_wait_for_message_response()
IDR:scmi_protocols
mark_txdone() op
e.g. virtio_mark_txdone()
0x10: scmi_base
0x11: scmi_power
….
0x14: scmi_clock
…
scmi_wait_for_reply()
fetch_response() op
e.g. scmi_optee_fetch_response()
Info->desc->ops->mark_txdone()
do_xfer_with_response()
[*async: delayed response]
fetch_notification() op
e.g. mailbox_fetch_notification()
Wait xfer→async_done until timeout
When rx-data is present,
call scmi_rx_callback()
[*channel-specific handling]
scmi_rx_callback()
[*async: delayed resp / notification ]
scmi_handle_response
Complete flags:
xfer→done, xfer->async_done
scmi_handle_notification

---
MISC Topics

---
SCMI-based Platforms
- stm32mpu (Linux, SCP, TF-A, op-tee)
- Juno ARM dev board (Linux, SCP)
- Rockchip rk3588/356x
- NXP I.MX8ULP
- SynQuacer (SCP, TF-A)
- NXP S32G (TF-A in downstream)
- Renasas R-car, N1SDP, SGM-775/776, SGI-575 …, etc.
  - Mainly in SCP

---
Some limitations
- Support common operations only
  - Complicated operations are not preferred. e.g. set/get parent clocks.
- Need more protocols to cover all available hardware resources in the real world
  - Battery, thernal, I/O, …, etc that ACPI has.
- Less platform code in upstream except SCP.

---
Limitations
Cmmon ops only
Complicated operations is not preferred.
E.g. Get/Set parent clocks ops
Number-based IDs
Need more protocols
E.g. battery, thermal, I/O … etc that ACPI has.
Less plat code upstreaming
Only a few plat implementations get upstreamed.